## Slide 1: SHA-3 version 1.0
16 March 2017

## Slide 2
SHA3
ready_o
md_valid_o
md_data_o[0:255]
clk_i
reset_i
start_i
squeeze_i
bitlen_i[10:0]
mode_sel_i[2:0]
md_ack_i
data_i[0:1599]

## Slide 3
State register[0:1599]
Input Message Stream Left
R-bits
R-bits
R-bits
R-bits
R-bits
r-bits
pad10*1
Endian byte swap
R + C-bits
B-bits
1 0
B-bits: Keccak-p permutation bit width (1600).
R-bits: RATE of sponge function in bits.
r-bits: remaining bits of message to hash
C-bits: capacity of sponge function
Rnd(A): round function of Keccak-p consisting of
5 step mappings (theta, rho, pi, chi, zeta).
RATEBITS: depends on the mode_sel_i value.
See mode_sel_i definition.
Rnd(A)
R-bits
B-bits
Control
mode_sel_i[2:0]
clk_i
reset_i
start_i
squeeze_i
bitlen_i[10:0]
md_ack_i
md_valid_o
ready_o
data_i[0:1599] = R-bits || (C-bits=0) (concatenated, left-justfified)
RATEBITS
start
ena
init
RoundIndex[4:0]
ena
5
11
start
3
mode_sel_i[2:0]
0 = shake128 (RATEBITS = 1344)
1 = shake256 (RATEBITS = 1088)
2 = sha3512 (RATEBITS = 576)
3 = sha3384 (RATEBITS = 832)
4 = sha3256 (RATEBITS = 1088)
5 = sha3224 (RATEBITS = 1152)
md_data_o[0:255]
init
RATEBITS[10:0]

## Slide 4
Direction | Signal | Width | Description
Input | clk_i |  | Global system clock
Input | reset_i |  | Global asynchronous active high reset
Input | mode_sel | [2:0] | Select mode SHA3. 0=shake128 (RATEBITS=1344) 1=shake256 (RATEBITS=1088) 2=sha3512 (RATEBITS=576) 3=sha3384 (RATEBITS=832) 4=sha3256 (RATEBITS=1088) 5=sha3224 (RATEBITS=1152)
Input | bitlen_i | [11:0] | Length of message on data_i to be hashed in bit count. Messages to be hashed can be an arbitrary long message. For messages >= RATEBITS which is selected by mode_sel, the messages are fed into SHA3.data_i in sections of bitlen_i=RATEBITS. Each section is hashed with a start_i pulse but no md_valid_o until the last section is hashed. When the last remaining section of the message is reached such that bitlen_i < RATEBITS, then the bitlen_i=remainder of message length and the md_valid_o goes active after the last section. For new messages that are less than the RATEBITS from the beginning, the bitlen=message length.
Input | start_i |  | 1=Start pulse to start SHA3 hashing. After receiving a valid start_i pulse, the ready_o goes low =0. The start pulse is ignored while ready_o=0 to ensure the current hash sequence is not disturbed. A start_i pulse is required to hash the next data_i even if the data_i is part of a multi-section message.
Input | squeeze_i |  | 1=squeeze additional md_data_o from the current data_i without re-issuing the start_i pulse. After 1 clock cycle of squeeze, md_data_o will be valid with md_valid_o=1. The squeeze pulse is ignored while ready_o=0 to ensure the current hash sequence is not disturbed.
Input | data_i | [0:1599] | Width 1600 matches with the width of the KECCAK-p permutation bits in sha3. But the actual valid data_i used is the size specified by bitlen_i starting from the left-most bit position of data_i; any remaining unused data_i[x] should be 0. Data to be hashed must be connected left-justified. For example, a message[0:23] (with bitlen=24) must be connected to Data_i[0:23] and the rest of Data_i[bitlen:1599]=0. Data_i must be valid and stable at the time start_i puse is received and must hold its value until ready_o=0.
Input | md_ack_i |  | Can be used as handshake with md_valid_o to throttle data output. If not used, connect to md_valid_o.

## Slide 5
Direction | Signal | Width | Description
Output | md_valid_o |  | 1=valid Message Digest. Will remain active high until md_ack_i=1 or a start_i=1 pulse is received. A md_valid_o=1 will occur 25 clocks after a start_i pulse when bitlen_i < RATEBITS as specified by mode_sel. At the time of start_i pulse when bitlen_i = RATEBITS which indicates a multi-section message, the md_valid_o will not go active =1 after 25 clocks. The md_valid_o will go active only after the last section of the multi-section message when bitlen<RATEBITS.
Output | ready_o |  | 1=sha3 module is ready for next message. Can be used as handshake with start_i pulse to help throttle input data_i. While ready_o=0, the start_i and squeeze_i are ignored.
Output | md_data_o | [0:511] | md_data_o is valid when md_valid_o=1. The md_data_o will remain valid even after md_valid_o=1 but before a start_i pulse. Depending on the mode_sel, the valid MD data will be left-justified of md_data_o as indicated below. For mode_sel = shake128, valid MD = md_data_o[0:127] For mode_sel = shake256, valid MD = md_data_o[0:255] For mode_sel = sha3512, valid MD = md_data_o [0:511] For mode_sel = sha3384, valid MD = md_data_o [0:383] For mode_sel = sha3256, valid MD = md_data_o [0:255] For mode_sel = sha3224, valid MD = md_data_o [0:223]

## Slide 6: Case 1: Len < RATEBITS (for SHA3256, RATEBITS = 1088; Len is length of input message to hash) Example below, Len = bitlen = 512; RATEBITS = 1088
Len=512, RATEBITS=1088
Start pulse
md_valid
25 clock cycles
Len < RATEBITS, so
Bitlen_i = Len = 512
Since Len of message < RATEBITS (512 < 1088), md_valid_o is valid after start_i pulse and 25 clock cycles.
25 clocks cycles consist of 24 rounds + 1 cycle load.

## Slide 7: Case 2a: Len = RATEBITS (for SHA3256, RATEBITS = 1088; Len is length of input message to hash) Example below, Len = 1088; RATEBITS = 1088
Len=1088, RATEBITS=1088
Start pulse
md_valid_o
2x25=50 clock cycles
Bitlen_i = Len-RATEBITS = 0
NO md_valid_o ,
Start pulse for next data of same message
Len = RATEBITS, so
Bitlen_i = Len = 1088 (max)
Since Len of message = RATEBITS (1088 = 1088), md_valid_o is valid after start_i pulse and 50 clock cycles.
50 clocks cycles consist of 2x of (24 rounds + 1 cycle load).

## Slide 8: Case 2b: Len > RATEBITS (for SHA3256, RATEBITS = 1088; Len is length of input message to hash) Example below, Len = 2184; RATEBITS = 1088
Len=2184, RATEBITS=1088
Start pulse
md_valid_o
3x25=75 clock cycles
Len>RATEBITS, so Bitlen_i = 1088
NO md_valid_o ,
Start pulse for next data of same message
Len 2184 – 1088 = 1096 (> RATEBITS), so
Bitlen_i = 1088 again
1096 – 1088 = 8 (< RATEBITS), so
Bitlen_i = 8
Since Len of message > RATEBITS (2184 > 1088), md_valid_o is valid after start_i pulse and 75 (3x25) clock cycles.
3x25 clocks cycles consist of RoundUp(Len/RATEBITS) x (24 rounds + 1 cycle load). (ie RoundUp(2184/1088)=3. x 25clocks).

## Slide 9: Squeeze additional md_data_o (without start_i pulse)
squeeze_i=1
md_valid_o=1
(from squeeze)
md_data_o valid
squeeze_i=1
md_valid_o=1
(from squeeze)
md_valid_o=1
From data case Len=2176
Squeeze_i is only valid while ready_o=1.
Squeeze_i should only be used after the first message has been hashed.
md_valid_o=1 on next clock cycle after a valid squeeze_i.
Does not require a start_i pulse.